## Slide 1: Earthquake Hazards
UT GEO 302P – Spring 2021
Part III – Lecture #4, March 23, 2020
Prof. Thorsten Becker
Reading: Ch. 3 & 4

## Slide 2: Last week

## Slide 3: The Parkfield M6 sequence
?

## Slide 4: The Parkfield CA prediction: expect M6 between 1988-1993

## Slide 5: 2004 M6 was 11 years too late

## Slide 6: 2004 M6 was 11 years too late (49% of ~23 yr period)

## Slide 7: Seismic hazard
Earthquakes cannot be predicted (yet) in terms of their time and space of occurrence
This means we need a probabilistic forecast of earthquake hazards
Seismic hazard: the likelihood and intensity of strong ground motion and other damaging effects at any location.

## Slide 8: Seismic hazard
The likelihood of strong ground motion and other damaging effects at any location.
Example:
  How likely is it to exceed 50% of the gravitational acceleration, g, in the next 50 years?

## Slide 9: Hazard and risk
Seismic hazard: the likelihood and intensity of strong ground motion and other damaging effects at any location
    How likely is it to exceed 50% of g in the next 50 years?
Seismic risk: the likelihood of seismically induced loss of life and property at any location
  How likely are losses of life (or $) in the next 50 years?

## Slide 10: Hazard and risk
Seismic hazard: the likelihood and intensity of strong ground motion and other damaging effects at any location
Seismic risk: the likelihood of seismically induced loss of life and property at any location
  Risk = hazard  exposure  vulnerability

## Slide 11: Hazard and risk
Seismic hazard: the likelihood and intensity of strong ground motion and other damaging effects at any location
Seismic risk: the likelihood of seismically induced loss of life and property at any location
  Risk = hazard  exposure  vulnerability

## Slide 12: Historical perspective on US hazard
What is the hazard in the US?
Why most in CA and AK?

## Slide 13
Why do the
quakes happen
where they do?

## Slide 14
Earthquakes happen
on faults…
Assess hazard by
generating seismicity catalogs
mapping faults

## Slide 15: How do we convert the knowledge about spatio-temporal seismicity characteristics into useful information for society?
Spatial information
frequency-magnitude information

## Slide 16: Understanding different types of hazards Primary hazards: Damage through fault offsets
Chi Chi earthquake Taiwan,
1999, Mw = 7.7 (2415 deaths, $10b damage)

## Slide 17: Primary hazards: Ground shaking
Mw = 7.6, 1999 Izmit:
shaking damage in Golcuk
(45,000 deaths,
20,000 buildings collapsed,
120,000 buildings damaged
beyond repair)

## Slide 18: Kobe, Japan 1995
Mw = 7
6,434 people died
~$90b, 2.5% of GDP at the time
Widespread structural failure, even for highest standard building codes

## Slide 19: Hazard due to mainshock and aftershocks
Loma Prieta M 7.1 1989

## Slide 20
Loma Prieta M 7.1 1989 aftershocks
frequency – magnitude relationship
for aftershocks

## Slide 21
Aftershocks of the
1989 Loma Prieta M7
Loma Prieta M 7.1 1989 aftershocks
Time-dependence
(decay of number of aftershocks/time)
frequency – magnitude relationship
for aftershocks

## Slide 22: Omori’s law
70
70/2 = 35
70/4 = 17.5
70/8=8.8
70/10=7.0
70/20=3.5
Aftershocks of the
1989 Loma Prieta M7
Aftershocks of
2011 Tohoku-oki M9
N(aftershocks) ~ 1/time
N(aftershocks) ~ 1/time

## Slide 23: Aftershock statistics
Omori’s law:
  number decreases as 1/time since mainshock
Bath’s law:
  largest aftershock is ~1.2 M units smaller than mainshock

## Slide 24
Earthquakes don’t kill people,
buildings do.

## Slide 25: What to do in an earthquake?

## Slide 26: Secondary hazards: Landslides
Nevado de Huascaran, Peru, 1970
Triggered by Ancash M = 7.9, off the coast

## Slide 27: Earthquakes perturb (critically stable) hillsides

## Slide 28: Major hazard for mountainous regions, including Pacific NW
Landslides due to M7.8 Ghorka, 2015
Roback et al. (2018)

## Slide 29: Water saturation important factor

## Slide 30: Differential settling due to liquefaction

## Slide 32: Secondary hazards: Liquefaction
Requires loose soils (sand or silt) and fluids
When shaken above a certain, critical level, soils may then lose all strength and flow
Areas with high ground water and loose soils (saturated) at risk, earthquake shaking is the trigger

## Slide 33: Secondary hazards: fires
San Francisco, 1906, Mw = 7.8

## Slide 34: Secondary hazards: fires
Northridge, 1995, Mw = 6.7

## Slide 35: Secondary hazards: Tsunamis
Banda Aceh 2004, Mw = 9.3
Lecture #5 will be on tsunamis.

## Slide 36: Seismic hazards
Primary hazards
  Ground shaking – regional impact
    Mainshock and aftershocks
  Surface displacement due to fault offset
Secondary hazards
  Tsunamis – hemispheric impact
  Landslides
  Soil liquefaction
  Fire
  Epidemics

## Slide 37: Assessing hazards: Ground shaking is measured from intensity (MMI) or peak ground acceleration (PGA)
What governs this distribution?
Mw = 7.3, 1992 Landers, California

## Slide 38: Predicting ground shaking for a potential earthquake, need to know:
Earthquake size
Earthquake distance (depth)

## Slide 39: What is the largest possible earthquake for a given site?
Two approaches…

## Slide 40: What is the largest possible earthquake for a given site?
Statistical: Gutenberg-Richter
Deterministic: Find the biggest fault (and convert to moment)
Biggest possible event M~10.5

## Slide 41: Determining the biggest local fault: Lessons from Landers 1992

## Slide 42
Faults can link up – earthquakes can jump from fault to fault
3 x M6.8 ~ Mw = 7.3

## Slide 43: Decay of shaking with distance
Geometric effect (wave energy distributed over larger volume)
Attenuation (= damping)
  due to dissipation (non elastic)
  depends on frequency

## Slide 44: Attenuation relationships
Li et al. (2012)
for Taiwan
Describe decrease of shaking
intensity with distance

## Slide 45: Significant shaking for similar size earthquakes: differences in attenuation because of geology

## Slide 46: Ground motion amplification

## Slide 47: Ground motion amplification
Seismic wave (force)
Seismic wave (force)
weak rock – large shaking
strong rock – small shaking

## Slide 48: Ground motion amplification

## Slide 49: Ground amplification: Attenuation relationships for different rock types
VS30 = integrated shear wave velocity over top 30 m – a proxy for rock strength
Li et al. (2012)
for Taiwan

## Slide 50: Site effects: Homogeneous half-space response to earthquake source

## Slide 51: Los Angeles sedimentary basin

## Slide 52: Site effects: LA basin response to source

## Slide 53: Resonance

## Slide 54: Resonance
many systems can oscillate, at given (“natural”) frequency (also called eigenfrequency)
when forced at frequencies that are too high or too low, compared to that frequency, amplitudes of oscillation don’t grow
when forced close to natural frequency, oscillations can amplify the amplitude of forcing greatly
Natural structures (e.g. sedimentary basins) and man made structures (e.g. high rise buildings) have natural frequencies

## Slide 55: Physics of ground shaking
Locally, the intensity is mainly determined by the earthquake size, type, and distance from hypocenter
Other contributions arise from
  regional damping/attenuation (tectonic setting)
  local site effects
    Amplification
    Basin resonance
  physics of rupture (one size earthquake can cause different shaking patterns, e.g. depending on direction/directivity)